IOM Mainsail Roach and Batten Control

Background

Originally the intention was that IOM mainsail roach control should be achieved by regulating the batten pocket positions and requiring the leech not to extend beyond straight lines between pockets, between the upper pocket and the aft head point and the lower pocket and the clew point. The same approach used by many ISAF classes.

A possibility for battens without batten pockets was however introduced and the “straight lines” were then to interlink at “batten pocket points” found at the intersection of the leech and the centreline of the batten pocket, or the batten when no pocket. This forced the leech to have a “peak” at each “batten pocket point”. But when such a peak becomes “rounded” by tear and wear the sail will become illegal as the leech will then project aft of the straight lines meeting at the batten pocket point.

- A way to solve the problem is to create “zones” at battens, or batten pockets, where the leech is not controlled by the straight lines. Similar to what is achieved when the straight lines are taken “between the pockets” as described in the first paragraph.

Proposed Class Rules Amendments

Goals for the proposed amendments:

•	To remove non ERS definitions if possible.

•	To amend the current, and in practise impossible, leech requirements.

•	To permit batten patches and to treat them equal to batten pockets.

- To permit mainsails without any battens/batten patches

•	To simplify the current leech control rules if possible.

- To legalize currently used sails which do not comply with the current rules in regard to leech shape at a batten pocket point and/or have batten patches.

Proposed amendments are included at the end of the document.

Comments on Batten Pockets and Battens without Pockets

There are currently a large numbers of mainsails with battens having one patch at its forward end and another at its aft end. It is not likely that such patches would qualify as a batten pocket and in any case only one would be permitted.

If batten patches are to be permitted, then it is difficult to see why the combined total area of patches should be required to be less than what is permitted for a batten pocket. And as a batten pocket may consist of any number and type of additional ply, why not allow the same for batten patches? And in view of what is permitted for batten pockets, why not have the same size restrictions for battens (stiffening) as for batten pockets?

26 December 2010

Prepared by Robert Grubiša, IOM ICA VC Chairman

(based on original proposal made by Jan Dejmo and comments received on informal meeting with sailmakers and IOM ICA Exec representatives during European Championship 2010 in France)

Section G – Sails

G.1	Parts

G.1.1	Mandatory

(a)	Mainsail.

(b)	Headsail.

G.2	General

G.2.1	Rules

Sails shall comply with the class rules in force at the time of their initial certification control.

G.2.2	Certification

(a)	The official measurer shall certify sails in the tack and shall date each with the date of certification control.

(b)	An MNA may appoint one or more persons at a sailmaker to measure and certify sails produced by that manufacturer. A special licence shall be awarded for that purpose.

G.2.3	Sailmakers

No licence is required.

G.2.4	DEFINITIONS

Batten  Point

The batten  point is defined as the intersection of the leech and

(a) the extended centreline of the batten or

(b) a line of minimum length 20 mm marked on the leech if there is no batten .

G.2.5	Measurement

(a)	During measurement:

(1)	battens need not be removed,

- mainsails with the luff not set in a mast spar track may be attached to spars,

- a headsail stay and mainsail mast spar jackstay need not be removed.

(b)	Where a mainsail has a luff bolt rope the luff shall be taken as the aft edge of the bolt rope.

(c)	Luff slides shall be ignored when measuring sail dimensions provided that their total length, measured along the luff, does not exceed 10% of the luff length.

G.3	Mainsail

G.3.1	Construction

(a)	MANDATORY

(1)	The construction shall be: soft sail, single ply sail.

(2)	The body of the sail shall consist of the same ply throughout and of not more than four parts joined by seams.

(3)	Seams shall not deviate more than 10 mm from a straight line between luff and leech.

(4)	The sail shall have three  battens at the leech or lines marked on the leech as defined in G.2.4(b) if there are no battens

(5)	Except within the leech stiffening zones, see H.3, the leech shall not extend aft of straight lines between :

(i)	the aft head point and the nearest batten  point,

(ii)	adjacent batten  points,

(iii)	the clew point and the nearest batten  point.

where the batten  points are to be taken as defined in G.2.4.

(6)	The foot shall not extend below a straight line between tack point and clew point.

(7)	Class insignia.

(b)	OPTIONAL

(1)	Tabling, which at the luff may form a pocket for a mast spar jackstay.

(2)	One or two cringles and/or openings at the head.

(3)	One cringle and/or openings at each of the clew and tack.

(4)	Luff openings for mast spar rings and/or loops for mast spar jackstay fittings.

(5)	Luff bolt rope.

(6)	Luff track slides.

(7)	Luff fittings for mast spar rings and/or loops.

(8)	Luff fittings for mast spar jackstay.

(9)	Primary reinforcement specified at G.3.3.

(10)	Secondary reinforcement specified at G.3.3.

(11) Primary reinforcement and/or stiffening within the leech stiffening zones defined by templates shown in H.3..

(12)	Tell tales.

(13)	Not more than three sail shape indicator stripes, applied using paint or ink.

(14)	Sailmaker labels.

G.3.2	Construction TECHNIQUES

(a)	Only the following construction techniques shall be used where parts are joined or added as permitted in G.3.1 and G.3.3: welding; gluing; bonding with self adhesive tapes/materials; stitching.

(b)	Except for stitching, the joining techniques used at seams shall not extend beyond the edges of the seam.

G.3.3 	Dimensions

minimum	maximum

Leech length:

mainsail 1 	 1610 mm 	 1620 mm

mainsail 2 	 1200 mm 	 1210 mm

mainsail 3 	 910 mm 	 920 mm

Foot length:

mainsail 1 	 350 mm 	 360 mm

mainsail 2 	 340 mm 	 350 mm

mainsail 3 	 310 mm 	 320 mm

Quarter width:

mainsail 1 	 305 mm 	 315 mm

mainsail 2 	 295 mm 	 305 mm

mainsail 3 	 265 mm 	 275 mm

Half width:

mainsail 1 	 235 mm 	 245 mm

mainsail 2 	 225 mm 	 235 mm

mainsail 3 	 205 mm 	 215 mm

Three-quarter width:

mainsail 1 	 135 mm 	 145 mm

mainsail 2 	 130 mm 	 140 mm

mainsail 3 	 115 mm 	 125 mm

Top width 		 20 mm

Primary reinforcement:

from nearest sail corner measurement point 		 125 mm

Secondary reinforcement:

from nearest sail corner measurement point 		 125 mm

for flutter patches 		 50 mm

at luff fittings, luff slides and/or luff openings 		 20 mm

Tabling width 		 15 mm

Seam width 		 15 mm

Seam to nearest sail corner measurement point 	 150 mm

Batten length:

middle and lower 		 100 mm

upper 		 75 mm

Batten width 		 10 mm

Batten  point, as defined in G.2.4, to nearest

leech point 		 20 mm

Largest cringle dimension 		 10 mm

With the exception for luff slides, largest luff fitting
dimension 		 10 mm

Sail shape indicator stripe width 		 30 mm

G.4	Headsail

G.4.1	CONSTRUCTION

(a)	MANDATORY

(1)	The construction shall be: soft sail, single ply sail.

(2)	The body of the sail shall consist of the same ply throughout and of not more than three parts joined by seams.

(3)	Seams shall not deviate more than 10 mm from a straight line between luff and leech.

(4)	Except within the leech stiffening zones, see H.3, the leech shall not extend aft of a straight line between the aft head point and the clew point.

(5)	The foot shall not extend below a straight line between tack point and clew point.

(b)	OPTIONAL

(1)	Tabling, which at the luff may form a pocket for a headsail stay.

(2)	One or two cringles and/or openings at the head.

(3)	One cringle and/or openings at each of the clew and tack.

(4)	Headsail stay slides and/or loops.

(5)	Primary reinforcement specified at G.4.3.

(6)	Secondary reinforcement specified at G.4.3.

(7)	Not more than two battens  at the leech.

(8)	Primary reinforcement and/or stiffening within the leech stiffening zones defined by templates as shown in H.3.

(9)	Tell tales.

(10)	Not more than two sail shape indicator stripes, applied using paint or ink.

(11)	Sailmaker labels.

G.4.2	Construction TECHNIQUES

(a)	Only the following construction techniques shall be used where parts are joined or added as permitted in G.4.1 and G.4.3: welding; gluing; bonding with self adhesive tapes/materials; stitching.

(b)	Except for stitching, the joining techniques used at seams shall not extent beyond the edges of the seam.

G.4.3	Dimensions

minimum	maximum

Luff length:

headsail 1 	 1320 mm 	 1330 mm

headsail 2 	 980 mm 	 990 mm

headsail 3 	 730 mm 	 740 mm

Leech length:

headsail 1 	 1245 mm 	 1255 mm

headsail 2 	 900 mm 	 910 mm

headsail 3 	 655 mm 	 665 mm

Foot length:

headsail 1 	 375 mm 	 385 mm

headsail 2 	 340 mm 	 350 mm

headsail 3 	 290 mm 	 300 mm

Half width:

headsail 1 	 185 mm 	 195 mm

headsail 2 	 165 mm 	 175 mm

headsail 3 	 140 mm 	 150 mm

Top width 		 20 mm

Primary reinforcement:

from nearest sail corner measurement point 		 125 mm

Secondary reinforcement

from nearest sail corner measurement point 		 125 mm

for flutter patches 		 50 mm

at headsail stay slides and/or loops 		 20 mm

Tabling width 		 15 mm

Seam width 		 15 mm

Seam to nearest sail corner measurement point 	 100 mm

Batten length 		 75 mm

Batten width 		 10 mm

Clew point to lower batten  point as defined in G.2.4:

headsail 1 	 400 mm 	 430 mm

headsail 2 	 285 mm 	 315 mm

headsail 3 	 205 mm 	 235 mm

Clew point to upper batten  point as defined in G.2.4:

headsail 1 	 820 mm 	 850 mm

headsail 2 	 590 mm 	 620 mm

headsail 3 	 425 mm 	 455 mm

Largest cringle dimension 		 10 mm

Sail shape indicator stripe width 		 30 mm

Part III – Appendices

H.3	 	LEECH STIFFENING ZONE

H.3.1	DEFINITION

A leech stiffening zone is a part of a sail that may be covered by a leech stiffening zone template as described in H.3.2 and positioned as described in H.3.3.

H.3.2	TEMPLATE AND TEMPLATE DATUM POINT

Leech stiffening zone template	Length, L

Mainsail middle and lower………………………………	120

Mainsail upper and headsail template……………………	95

H.3.3	TEMPLATE POSITIONING

It shall be possible to position the template so that

(1)	its datum point is over the relevant batten point,

(2)	its long edges cut the leech and

(3)	it covers any primary reinforcement and/or stiffening.