| INTERNATIONAL ONE METRE CLASS |  |  | 2007 |
| --- | --- | --- | --- |
| RIG/SAIL MEASUREMENT FORM |  |  |  |
| RIGS AND ITS SAILS MEASURED (cross out as appropriate) | 1 | 2 | 3 |

Hull Registration Number 						   .................................................

GENERAL NOTE TO MEASURERS

1	Measurements shall be carried out in accordance with the Equipment Rules of Sailing except where varied in the class rules.

2	The boat shall comply with all the class rules in Sections D, E, F,G and H even if some of the rules are not mentioned on the measurement form(s).

3	This measurement form may be used for up to three rigs and its sails. Cross out the numbers above for rigs and its sails which have not been measured. Ring the numbers which have been measured.

4	To have more rigs and its sails added to the certificate the official measurer shall measure the rigs and its sails and complete a new rig/sail measurement form. The rig/sail measurement form, together with any re-certification fee that may be required and the current certificate shall be sent to the owner’s certification authority.

| PARTS |
| --- |
| 1 | F.1.1 | Does any rig comprise more than: one mast, one mainsail boom, one headsail boom, standing rigging, running rigging and fittings? | yes / no |
| GENERAL |
| 2 | F.2.3 | Do all parts of the rig function in a way that is normal for items of their type? | yes / no |
| 3 | F.2.4(c) | Are any ball and/or roller bearings used in any items except for: kicking strap fitting, gooseneck, mainsail boom sheet blocks, headsail boom sheet blocks, headsail boom swivel? | yes / no |
| MAST |
| 4 | F.3.1(a) | Is the principal material of the spar aluminium alloy or wood? | yes / no |
| 5 | F.3.1(b) | Are other materials on the spar limited to: adhesive, paint, powder coat, varnish, wax? | NA / yes / no |
| 6 | F.3.2(b) | Is the spar section between upper point and lower point: of circular outer shape and constant except for: internal sail track, local cutaways, openings for fittings and/or rigging, internal and/or external spar joiners? | yes / no |
| 7 | F.3.3(a) | Are the fittings listed in class rule F.3.3(a) present? | yes / no |
| 8 | F.3.3 | Are there any fittings except items listed in class rules F.3.3(a) & (b)? | yes / no |
| 9 | F.3.3(c)(2) | Do the mainsail boom spar and the kicking strap have pivot points aft of the mast spar in the regions adjacent to these points? | yes / no |
| 10 | F.3.4 | Is the lower point to upper point dimension correct? |
|  |  | rig 1 1600 mm max | rig 2 1180 mm max | rig 3 880 mm max | yes / no |
| 11 | F.3.4 | Is the lower edge of the headsail stay limit mark at the foreside of the spar to the upper point dimension correct? |  |
|  |  | rig 1 220 mm min | rig 2 160 mm min | rig 3 120 mm min | yes / no |
| 12 | F.3.4 | Does the height of checkstay rigging point above the heel point exceed 100 mm? | NA / yes / no |
|  | F.3.4 | Between lower point and upper point: |
| 13 |  | (1) Is the diameter of the spar less than 10.6 mm? | yes / no |
| 14 |  | (2) Does the difference between the largest and smallest diameters exceed 0.3 mm? | yes / no |
| 15 | F.3.4 | Does the length of any spar joiner exceed 100 mm? | yes / no |
| 16 | F.3.4 | Does the total length of cutaways between the lower point and upper point exceed 100 mm? | yes / no |
| 17 | F.3.4 | Is the width of all limit marks between 3 and 10 mm? | yes / no |
| BOOMS |
| 18 | F.4.1(a) | Is the principal material of the spars aluminium alloy or wood? | yes / no |
| 19 | F.4.1(b) | Are other materials on the spars limited to: adhesive, paint, powder coat, varnish, wax? | NA / yes / no |
| 20 | F.4.2 | Is the section of spars constant except for the last 10 mm at each end and openings for fittings and rigging? | yes / no |
| 21 | F.4.3-4 | Are the fittings listed in class rules F.4.3(a) and F.4.4(a) present? | yes / no |
| 22 | F.4.3-4 | Are there any fittings except items listed in class rules F.4.3 & F.4.4? | yes / no |
|  | F.4.5 | Ignoring the last 10 mm at each end and openings for fittings and rigging: |
| 23 |  | Does the largest external dimension exceed 20 mm? | yes / no |
| 24 |  | Does the difference between the smallest and largest value along the spar of any external dimension exceed 0.5 mm? | yes / no |
| STANDING RIGGING |
| 25 | F.5.1 | Except for terminations and the headsail boom swivel, are there any materials except steel and/or polymer? | yes / no |
| 26 | F.5.2(a) | Is the standing rigging listed in class rule F.5.2(a) present? | yes / no |
| 27 | F.5.2-3 | Is there any standing rigging except items listed in class rules F.5.2 and F.5.3? | yes / no |
| RUNNING RIGGING |
| 28 | F.6.2(a) | Is the running rigging listed in class rule F.6.2(a) present? | yes / no |
| 29 | F.6.2-3 | Is there any running rigging except items listed in class rules F.6.2 and F.6.3? | yes / no |
| MAINSAILS |
| 30 | G.2.2(b) | If the sails have been certified by the manufacturer awarded with a special licence, indicate here and ignore steps 31 to 58. | yes / no |
| 31 | G.3.1(a)(1) | Are all sails soft sails and single ply sails? | yes / no |
| 32 | G.3.1(a)(2) | Does the body of the sail consist of the same ply throughout and not more than four parts joined by seams? | yes / no |
| 33 | G.3.1(a)(3) | Do seams deviate by more than 10 mm from a straight line between luff and leech? | yes / no |
| 34 | G.3.1(a)(4) | Does each sail have three batten pockets, or battens if there are no batten pockets, at the leech? | yes / no |
| 35 | G.3.1(a)(5) | Does the leech extend aft of straight lines between: adjacent batten pocket points, sail corner measurement points and nearest batten pocket points? | yes / no |
| 36 | G.3.1(a)(6) | Does the foot extend below a straight line between tack point and clew point? | yes / no |
| 37 | G.3.1(a)(7) | Is a class insignia present? | yes / no |
| 38 | G.3.1(b) | Are there any parts except items listed in class rule G.3.1(b)? | yes / no |
| 39 | G.3.2(a) | Are the parts of the sails joined or added using only welding; gluing;bonding with self- adhesive tapes/materials; stitching? | yes / no |
| 40 | G.3.2(b) | Except for stitching, does the method used to join the seams extend beyond the edges of the seams? | yes / no |
| 41 | G.3.3 | Does the upper batten exceed 10 mm wide x 75 mm long, and/or its batten pocket exceed 25 mm wide x 95 mm long? | yes / no |
| 42 | G.3.3 | Do the other battens exceed 10 mm wide x 100 mm long, and/or their batten pockets exceed 25 mm wide x 120 mm long? | yes / no |
|  | G.3.3 | Are the following primary sail dimensions within the permitted ranges? |  |
|  |  | Leech Length |
| 43 |  | 1 1610-1620 mm | 2 1200-1210 mm | 3 910-920 mm | yes / no |
|  |  | Foot Length |
| 44 |  | 1 350-360 mm | 2 340-350 mm | 3 310-320 mm | yes / no |
|  |  | Quarter Width |
| 45 |  | 1 305-315 mm | 2 295-305 mm | 3 265-275 mm | yes / no |
|  |  | Half Width |
| 46 |  | 1 235-245 mm | 2 225-235 mm | 3 205-215 mm | yes / no |
|  |  | Three-Quarter Width |
| 47 |  | 1 135-145 mm | 2 130-140 mm | 3 115-125 mm | yes / no |
|  | G.3.3 | Are the following exceeded? |
| 48 |  | Top width | 20 mm | yes / no |
| 49 |  | Primary & secondary reinforcement from nearest sail corner measurement point | 125 mm | yes / no |
| 50 |  | Secondary reinforcement for flutter patches | 50 mm | NA / yes / no |
| 51 |  | Secondary reinforcement at luff fittings, luff slides and/or luff openings | 20 mm | NA / yes / no |
| 52 |  | Tabling width | 15 mm | yes / no |
| 53 |  | Seam width | 15 mm | yes / no |
| 54 |  | Seam to nearest sail corner measurement point | 150 mm | yes / no |
| 55 |  | Batten pocket point, as in G.2.4, to the nearest leech point | 20 mm | yes / no |
| 56 |  | Largest cringle dimension | 10 mm | yes / no |
| 57 |  | Except for luff slides the largest luff fitting dimension | 10 mm | NA / yes / no |
| 58 |  | Sail shape indicator stripe width | 30 mm | NA / yes / no |
| HEADSAILS |
| 59 | G.2.2 (b) | If the sails have been certified by the manufacturer awarded with a special licence, indicate here and ignore steps 60 to 83. | yes / no |
| 60 | G.4.1(a)(1) | Are all sails soft sails and single ply sails? | yes / no |
| 61 | G.4.1(a)(2) | Does the body of the sail consist of the same ply throughout and not more than three parts joined by seams? | yes / no |
| 62 | G.4.1(a)(3) | Do seams deviate by more than 10 mm from a straight line between luff and leech? | yes / no |
| 63 | G.4.1(a)(4) | Does the leech extend aft of a straight line between the aft head point and clew point? | yes / no |
| 64 | G.4.1(a)(5) | Does the foot extend below a straight line between tack point and clew point? | yes / no |
| 65 | G.4.1(b) | Are there any parts except items listed in class rule G.4.1(b)? | yes / no |
| 66 | G.4.2(a) | Are the parts of the sails joined or added using only welding; gluing; bonding with self- adhesive tapes/materials; stitching? | yes / no |
| 67 | G.4.2(b) | Except for stitching, does the method used to join the seams extend beyond the edges of the seams? | yes / no |
| 68 | G.4.3 | Does any batten exceed 10 mm wide x 75 mm long, and/or its batten pocket exceed 25 mm wide x 95 mm long? | NA / yes / no |
|  | G.4.3 | Are the following sail dimensions within the permitted ranges? |
|  |  | Luff Length |
| 69 |  | 1 1320-1330 mm | 2 980-990 mm | 3 730-740 mm | yes / no |
|  |  | Leech Length |
| 70 |  | 1 1245-1255 mm | 2 900-910 mm | 3 655-665 mm | yes / no |
|  |  | Foot Length |
| 71 |  | 1 375-385 mm | 2 340-350 mm | 3 290-300 mm | yes / no |
|  |  | Half Width |
| 72 |  | 1 185-195 mm | 2 165-175 mm | 3 140-150 mm | yes / no |
|  |  | Clew point to lower batten pocket point |
| 73 |  | 1 400-430 mm | 2 285-315 mm | 3 205-235 mm | NA / yes / no |
|  |  | Clew point to upper batten pocket point |
| 74 |  | 1 820-850 mm | 2 590-620 mm | 3 425-455 mm | NA / yes / no |
|  | G.4.3 | Are the following exceeded? |
| 75 |  | Top width | 20 mm | yes / no |
| 76 |  | Primary & secondary reinforcement from nearest sail corner measurement point | 125 mm | yes / no |
| 77 |  | Secondary reinforcement for flutter patches | 50 mm | NA / yes / no |
| 78 |  | Secondary reinforcement at headsail stay slides and/or loops | 20 mm | NA / yes / no |
| 79 |  | Tabling width | 15 mm | yes / no |
| 80 |  | Seam width | 15 mm | yes / no |
| 81 |  | Seam to nearest sail corner measurement point | 100 mm | yes / no |
| 82 |  | Largest cringle dimension | 10 mm | yes / no |
| 83 |  | Sail shape indicator stripe width | 30 mm | NA / yes / no |

DECLARATION BY THE OWNER To the best of my knowledge, the aluminium alloys used for the mast and boom spars are of the grades listed in F.3.1 and F.4.1 and the wall thickness tolerances in F.3.4 and F.4.5 are complied with. Any weights attached to the mast spar above the lower point are of a density not exceeding 8000 kg/m3.

Signature  	Date

................................................................. 	.................................................................

MEASURER'S COMMENTS

If the official measurer has any doubt concerning the application of, or compliance of any part of the boat with the class rules he shall report it on the measurement form(s) before sending them to the certification authority and not sign measurement form(s) or sails.

DECLARATION BY THE MEASURER

I confirm that I have taken the measurements on this form, that the particulars on this form are correct and that, to the best of my knowledge, the boat complies with the rules covered by this form. I have stated above in MEASURER`S COMMENTS those points where I have any doubt concerning the application of, or compliance of any part of the boat with, the class rules whether or not they are covered by the measurement form.

| Name of Measurer | Officially recognised by |
| --- | --- |
| (BLOCK CAPITALS) | (ISAF Member National Authority of Country) |
| ....................................................................................................................... | ....................................................................................................................... |
| Signature | Date |
| ....................................................................................................................... | ....................................................................................................................... |